## Slide 1: Industrial Internship Review BECE399J/ECE1902 Exploring the Potential of IoT with Sensor Network Enthu Technology Solutions India Pvt Ltd S.ASWATH 21BEC2188 B.TECH ECE SENSE

## Slide 2: INTERNSHIP CERTIFICATE

## Slide 3: Agenda of the presentation
Objective of this Internship
Organization information
Various Domains, I worked
  1. ESP 32 WDM Ver 2.0
  2. STM 32
  3. STM 32 Development Model
Communication Protocol.
Lora Wan Technology.
Experience Gained.
Summary.

## Slide 4: Objective: During my internship at Enthu Technology Solutions India Pvt Ltd, my objective was to study various aspects related to IOT such as Sensor interfacing with ESP32,Sensor interfacing with STM32 and Sensor interfacing with LoRaWAN and LoRaWAN technology, and Other different product of the company. Organization Information: Enthu Technology Solutions India Pvt. Ltd. is an ISO-Certified Organization founded by a group of young Entrepreneurs in 2007 and incorporated as a Private Limited Company in 2015. We offer best-in-class end-to-end Product Design, Development, and Manufacturing services for Embedded and IoT products. As a product development R&D company, we have in-house Hardware Design and Prototyping, Software Development, EMS Assembly, Enclosure Design & Manufacturing, IoT Cloud based Web & Mobile App Development, product testing, and Deployment. VIT has signed a MoU with Enthu technology. VIT is client of Enthu technologies. Enthu Academic Solutions (EAS) is an academic division of Enthu Technology Solutions has taken part in implementation of project based learning. Enthu tech established a Modern Industrial grade Laboratories with smart campus Infrastructure at PRP 108 in VIT.

## Slide 5: INTERNET OF THINGS(IOT)
INTERNET OF THINGS
The Internet of Things in These Days, Using Microcontrollers To Develop Various Low-Cost Systems Is Quite Popular. The primary goals of the Internet of Things are to reduce labour force or manpower and to conserve energy by reducing electricity waste.
IoT has applications in diverse fields, including smart homes, healthcare, agriculture, transportation, and industrial automation, revolutionizing how we interact with the world around us.

## Slide 6: ESP 32 WDM ver2.0
The ESP32 is widely used in IoT applications, including smart home devices, wearables, industrial automation, and more.
Its low power consumption, advanced features, and extensive development ecosystem make it a popular choice for embedded systems projects.
Programmable using the Arduino IDE , and other development environments
It has Wi-Fi, Bluetooth capability and it has in total of 48 pins.

## Slide 7
▶ Interfacing Sensor with ESP:
Performed some tasks by using some IoT sensors with hardware using ESP32 and the software platform Arduno IDE.
Interfacing sensors with the ESP32 using the Arduino IDE simplifies IoT development by providing a familiar and user-friendly environment for sensor integration and data processing.
Learn to program ESP32 microcontrollers using the Arduino IDE and ESP-IDF framework.
Understand ESP32 hardware features and capabilities, including Wi-Fi and Bluetooth connectivity.
Develop IoT applications leveraging the power and versatility of the ESP32 platform.

## Slide 8: SENSORS Used with ESP32
Gas sensor
LDR sensor
Ultrasonic Sensor
Soil moisture
sensor
Rain
drop sensor
Accelerometer(BH1750)
OLED Display

## Slide 9: COMMUNICATION PROTOCOLS
I2C protocol:
I2C stands for the inter-integrated circuit and it requires only two wires connecting all peripherals to the
microcontroller. I2C requires two wires SDA (serial data line) and SCL (serial clock line) to carry information between
devices. It is a master to a slave communication protocol. Each slave has a unique address. The master device sends
the address of the target slave device and reads/writes the flag. The address matches any slave device that the device
is ON, the remaining slave devices are disabled mode.
2. SPI protocol:
SPI stands for the serial peripheral interface. It is one of the serial communication protocol developed by Motorola.
Sometimes SPI protocol is also called a 4-wire protocol. It requires four wires MOSI, MISO, SS, and SCLK.SPI protocol
used to communicate the master and slave devices. The master first configures the clock using a frequency.

## Slide 10: COMMUNICATION PROTOCOLS BASED SENSORS
I2C protocol:
Accelerometer (BH1750)
2. SPI protocol:
OLED

## Slide 11: The STM32 is a series of 32-bit microcontrollers developed by STMicroelectronics, based on ARM Cortex-M processor cores.
STM 32
These microcontrollers are widely used in embedded systems, IoT devices, industrial automation, and consumer electronics due to their high performance, low power consumption, and rich peripheral integration.

## Slide 12: STM32
Performed Basics Program such as
▶ Printing of Hello world to to turn ON and turn OFF the Led
▶ Toggling of Led using PIR and TILT Sensor using STM32
Gain proficiency in programming STM32
microcontrollers using STM32CubeIDE
and HAL library.
Explore STM32 hardware peripherals and
functionalities for sensor interfacing motor
control, and communication protocols.
Develop embedded applications targeting
STM32 microcontrollers for diverse IoT
use cases.

## Slide 13: LORAWAN
▶ LoRaWAN is a long-range, low-power wireless communication protocol designed for IoT applications, offering connectivity over several kilometers in urban environments and even more in rural areas.
▶ With its low power consumption, wide coverage, and scalability, LoRaWAN enables cost-effective and efficient deployment of IoT networks for diverse use cases.

## Slide 14: LORAWAN USAGES
Learnt the principles and architecture of LoRaWAN for long-range wireless communication in IoT.
Understood LoRa modulation techniques and LoRaWAN protocol stack layers.
Implemented LoRaWAN end-device applications on ESP32 and STM32 platforms for transmitting sensor data over long distances.

## Slide 15: STM 32 WL development
kit with LoRaWan
The STM32WL development kit is a comprehensive platform provided by STMicroelectronics for developing IoT solutions based on the STM32WL series of microcontrollers, which integrate LoRa communication capabilities
Task done using STM32 WL dev kit with LoRaWan
▶ Basic program of relay turn on and turn off
▶ Basic program of LED turn ON and turn OFF

## Slide 16
Software Learnt:
1.Integrated Development Environment (IDE): STM32 IDE is an integrated development environment tailored for STM32 microcontrollers developed by STMicroelectronics and Arduino IDE tailored for ESP 32 mircrocontollers, cloud platforms like ThingSpeak, ThingsMate, Ubidots.
2.Based on Eclipse: It is built on the Eclipse platform, providing a familiar environment for developers.
3.Cross-Platform: Supports Windows, macOS, and Linux operating systems, ensuring compatibility across various platforms.
4.STM32CubeMX Integration: Integrated with STM32CubeMX, a graphical tool that allows users to generate initialization code and configure peripherals graphically.
5.Code Generation: Generates initialization code for peripherals, middleware, and application code, speeding up development.
6.Code Editing and Debugging: Offers features for code editing, syntax highlighting, code completion, and debugging functionalities, essential for efficient development and debugging processes.

## Slide 17
7.Peripheral Configuration: Provides tools for configuring and fine-tuning STM32 microcontroller peripherals, such as GPIOs, timers, UARTs, SPIs, etc.
8.HAL (Hardware Abstraction Layer) Library: Supports HAL library, a set of APIs abstracting low level hardware access, facilitating portability across different STM32 microcontroller families.
9.Real-Time Operating System (RTOS) Support: Integrates support for FreeRTOS, enabling developers to create applications with real-time capabilities.
10.Version Control Integration: Supports integration with version control systems like Git, allowing collaborative development and version tracking.
11.Community and Support: Access to a large community of developers, forums, and documentation, providing assistance and resources for troubleshooting and learning.
12.Updates and Maintenance: Regular updates and maintenance releases to incorporate bug fixes, improvements, and support for new STM32 microcontroller series and features.

## Slide 18
SMART STREET PROJECT USING WOKWI SOFTWARE

## Slide 19
My Experience with Enthu Technology Solutions .
Gain practical experience in embedded
systems development, IoT, and wireless
communication technologies.
Acquire proficiency in programming ESP32
and STM32 microcontrollers for diverse
applications.
Develop a deep understanding of LoRaWAN
technology and its role in IoT connectivity.
Collaborate with experienced engineers and
mentors to tackle real-world challenges in IoT
development.
Receive valuable feedback, guidance, and
networking opportunities for future career
advancement in the field of embedded systems
and IoT.

## Slide 20
Enthu Technology Solutions is a Indian Pvt. Limited company.
▶ They offer best-in-class end-to-end Product Design, Development, and Manufacturing services for Embedded and IoT products.
▶ As a product development R&D company, they have in-house hardware design and prototyping, software development, EMS assembly, enclosure design and manufacturing, IoT cloud-based web and mobile app development, product testing, and deployment.

## Slide 21: Summary
This internship provides a comprehensive hands-on experience in developing applications using ESP32 and STM32 microcontrollers with a focus on LoRaWAN technology.
Interns will gain practical skills in IoT device development, wireless communication protocols, and embedded systems programming.