## Slide 1: SMART STREET
PRESENTERS:
ASWATH S
MOHAMED ANAS
HENSILIN RITHISTA S
SIYAM A G
PRAISAN SMITH
MAYURESH ROHIT

## Slide 2: TABLE OF CONTENTS 01 02 03
SENSORS
DISPLAYS
CIRCUIT

## Slide 3: INTRODUCTION
The Internet of Things These Days Is Quite Popular In The Development Of Different Low-Cost Systems With The Help Of A Microcontroller. Main Aim Of The Internet Of Things Is To Conserve Energy By Reducing Wastage Of Electricity And Also To Reduce Labor Force Or Manpower. Streetlights Are Quite An Important Part Of A City Because It Helps In Giving Better Vision Of Roads And Streets At Night Time.

## Slide 4: SENSORS
DHT-22
Temperature and Humidity sensor
MPU-6050
Accelerometer and gyroscope
LDR light sensor
Detect and measure the amount of light.
PIR
Motion Sensor
01
03
02
04

## Slide 5: DHT-22
Operating Voltage-3 to 5V
Max Operating Current-2.5mA max
Humidity Range-0-100% / 2-5%
Temperature Range- -40 to 80°C / ± 0.5°C
Sampling Rate-0.5 Hz (reading every 2 seconds)
Body size-15.1mm x 25mm x 7.7mm
Advantage-More Accurate

## Slide 6: LDR light sensor
Advantage-More Accurate
Operating Voltage - 3.3V to 5V DC
Operating Current - 15ma
Output Digital - 0V to 5V, Adjustable trigger level from preset
Output Analog - 0V to 5V based on light falling on the LDR
PCB Size: 3.2cm x 1.4cm

## Slide 7: MPU-6050
Operating Voltage - 5V (typical)
Max Operating Current - less than 3.6mA
Accelerometer Range - ±2g, ±4g, ±8g, ±16g
Temperature Range - -40 to +85°C
Gyroscope Range - ±250°/s, ±500°/s, ±1000°/s, ±2000°/s
Absolute Maximum Acceleration - Up to 10,000g
Advantage - Low power consumption

## Slide 8: PIR
Operating Voltage - 4.5 – 20V (typically 5V)
Max Current Draw - < 2mA
Detection Distance - 3 – 7 meters (9 – 21 feet)
Detection Angle - 120 degrees (typically)
Time Delay - 1 sec to 3 min
Advantage - Low power, low cost, easy to interface

## Slide 9: DISPLAY
16*2 LCD Display
I2C OLED Display
01
02

## Slide 10: I2C OLED Display
Screen Size - 0.96 Inch Across
Screen Size - 128×64 pixels
Operating Voltage - 3.3V – 5V
Operating Current - 20mA max
Viewing Angle - 160°
Characters Per Row - 21
Number of Character Rows - 7

## Slide 11: 16*2 LCD Display
Screen Size - 85.0 x 29.5 x 13.5 mm
Screen Size – 32*40 pixels
Operating Voltage - 3.3V – 5V
Operating Current - 20mA max
Viewing Angle - 180°
Characters Per Row - 16
Number of Character Rows - 2

## Slide 12: CIRCUIT

## Slide 13: THANKS!